Rising Sun Phosphate Treatment

(Phosphate treatments may cloud water)

Phosfree – levels below 1000 ppm & pool clear

- Balance pool water

- If pool has algae follow instructions for algae treatment

- Backwash filter if necessary

- Determine required dosage of Phosfree from chart

Dose per 10,000 gallons

Phosphate Level (PPB)	Phosfree (in ounces)

300 or less			16 oz.

600				32 oz.

900				48 oz.

5. 	With filter running (shake bottle) & add _____of Phosfree to skimmer

6. 	Run filter continuously & backwash as needed. (Filter pressure will increase within 4-24 hrs.)

7. 	After one week retest phosphate levels & add approximately ____ of Phosfree each time source water is added to pool.  (.5oz per 10,000 gal)

** May require multiple treatments to eliminate phosphate levels **

Commercial Phosfree – levels over 1000 ppm & pool clear

(Same directions as Phosfree but different doses)

Dose per 20,000 gallons

Phosphate level				Phosfree (in ounces)

1000 or less					32 oz.

1000-2500					64 oz.

Over 2500					96 oz

# Phosfloc – levels over 1000 ppm & not clear

- Balance pool water

- Use 4 lbs. of Phosfloc per 10,000 gallons

- Dissolve ____ Phosfloc in a large bucket of water

- With filter system running on RECIRCULATE slowly pour

- Phosfloc mixture through skimmer.

- Allow system to run on RECIRCULATE for 1 hour

- Turn system OFF allow system to stay OFF  12-24 hours.

- When pool settles vacuum to WASTE- This step may need to be

- Repeated s few times.

- Check pool chemistry and rebalance as needed.

## Phosphate Remover

- Balance pool water.

- Pour ____ oz of Phosphate Remover over surface (32 oz per 10,000 gallons)

- Put 4 in 1 Clarifier Tablets in skimmer.

- Do not turn pump off, let the pump run at least 24 hours.

- When the pressure in the filter increase by 10 psi. backwash.

3-25-09