Super Drop N Floc

Instructions

Rising Sun Pools

- Adjust ph to 7.4 – 7.8

- Set filter on Re-circulate.

3.	Pour ________ oz of  SUPER DROP N FLOC around surface of pool.  Spread around as much as possible.

(1 qt per 40,000 gallons MINIMUM – can double up)

4.	Allow pump to run on Re-circulate for 1-2 hours.

- Turn the pump off and let the pool settle.  Leave the pump off for 12 – 48

hours until pool is completely clear.  No Swimming, Brushing, or

Disturbing Water Allowed during this time.

- Once the pool is clear, (there will be a film of debris at the bottom of the

pool) vacuum the pool to waste in sections, starting with the shallow end

first.  As soon as the pool clouds up turn the pump off again until it clears.

Then proceed to vacuum another section.  If the water gets low, turn the

pump off and refill..

Revive

(Can be used with all sanitizers)

- Turn pump off.

- Attach spray bottle to garden hose. Spray entire pool surface using all

contents of the bottle (16 oz bottle treats up 12k gallons. 32oz bottle treats   up to 24k gallons).

- Allow a minimum of 24 hours for debris to settle to bottom.

- Vacuum debris slowly to waste.

Notes

- If water clouds when vacuuming stop and let it settle back out.

- Make sure water level is higher than normal before doing any floc treatment.

- When vacuuming to waste it is best to vacuum in sections.

- If algae growth is present, treat algae before using floc.

- If metals are present before using a floc, staining is possible.

3-25-09